## Slide 1: Operational Amplifiers
EE 204

## Slide 2: BJT Applications
BJT Amplifier

## Slide 3: BJT Applications
Transistor is a switch (most common application)
BJT Amplifier (second most common…)

## Slide 4: What is an Op-Amp
Op-Amp or operational amplifier a modular circuit that is designed to work with other circuit elements (in boom boxes, speakers, cell phones, biomedical apps, sensors, heart rate monitors, power circuits, computers)
The simplest model of the operational amplifier is the ideal operational amplifier. (there are several models to define a “realistic op-amp)
Circuits that contain ideal operational amplifiers are analyzed by writing and solving node equations.
Operational amplifiers can be used to build circuits that perform mathematical operations.
  Summing Amplifier
  Difference Amplifier
  Current to voltage converter
  Voltage controlled Current Source

## Slide 5: Symbol and Equivalent Circuit
vd = v2 – v1
A is the open-loop voltage gain

## Slide 6: Ideal vs Real Op-Amp
Real Op-Amps have limits. Since they are made of transistors they can be saturated.
For an ideal Op-Amp we assume a three basic things (no saturation)
Parameter | Variable | Typical Ranges | Ideal Values
Open-Loop Voltage Gain | A | 105 to 108 | ∞
Input Resistance | Ri | 105 to 1013 W | ∞ W
Output Resistance | Ro | 10 to 100 W | 0 W
Supply Voltage | Vcc/V+ -Vcc/V- | 5 to 30 V -30V to 0V | N/A N/A
In real life you can find out the operating (linearity values from manufacturer)

## Slide 8: Caution – A is Frequency Dependent
http://www.national.com/ds/LM/LM124.pdf

## Slide 9: Ideal Op-Amp
Ri = ∞ Ω
  Therefore, i1 = i2 = 0A
Ro = 0 Ω
Usually, vd = 0V so v1 = v2
  The op amp forces the voltage at the inverting input terminal to be equal to the voltage at the non-inverting input terminal if there is some component connecting the output terminal to the inverting input terminal.
Rarely is the op amp limited to V- < vo < V+.
  The output voltage is allowed to be as positive or as negative as needed to force vd = 0V..

## Slide 10: Example #1: Inverting Amplifier
i2 = 0
i1 = 0
is
if
V+ = 15V
V- = -10V
i

## Slide 11: Example #1 (con’t)
i2 = 0
i1 = 0
is
if
V+ = 15V
V- = -10V
i
Closed loop gains are dependent on the values of R1 and Rf.
  Therefore, you have to calculate the closed loop gain for each new problem.

## Slide 12: Example #1 (con’t)
i2 = 0
i1 = 0
is
if
i
vo