## Slide 1
Transistors
First Transistor Model, 1947
FET Transistor
BJT Transistor
Transistors of various type & size
Used in all modern electronics
BJT (PNP) Electrical Diagram Representation
Notes: You’ve all seen the transistor before, but instead of regurgitation, provide student perspective….

## Slide 2
tran·sis·tor
a semiconductor device that amplifies, oscillates, or switches the flow of current between two terminals by varying the current or voltage between one of the terminals and a third. (www.dictionary.com)
www.coltecnica.com

## Slide 3
  Basic Purpose
  [1] To electronically switch (no moving parts) a signal on or off (high/low)
  [2] To amplify signals
  Role in Modern Electronics
    Basic building blocks for all modern electronics
    Microprocessors, Microcontrollers, Computers, Digital watches, Digital Logic Circuits, Cell Phones….
Microprocessor
PC & Cell Phones
Motor Controllers
Headphones
Notes: ROADMAP OF BUILD TRANSISTOR -> PROPERTIES

## Slide 4
Early 20th century, vacuum tube were used as signal amplifiers & switches.
Use of vacuum tube* resulted in extremely large, fragile, energy inefficient, and expensive electronics.
Evolution of electronics required device that was small, light weight, robust, reliable, cheap to manufacture, energy efficient…
*Vacuum tube advantages: operation at higher voltages (10K region vs. 1K region of transistors); high power, high frequency operation (over-the-air TV broadcasting) better suited for vacuum tubes; and silicon transistors more vulnerable to electromagnetic pulses than vacuum tubes
Reason for Transistor’s Invention:
Vacuum Tube Radios
ENIAC : 17, 468 vacuum tubes

## Slide 5
Invention
  In 1947, John Bardeen, Walter Brattain, and William Schockly, researchers at Bell Lab, invented Transistor.
  They found Transistor Effect: “when electrical contacts were applied to a crystal of germanium, the output power was larger than the input.”
  Awarded the Nobel Prize in physics (1956)
  Revolutionized portability and efficiency of electronic devices
John Bardeen, Walter Brattain, and William Schockly
First model of Transistor, 1947

## Slide 6: Model of a transistor
Bipolar transistors are constructed of a three-layer semiconductor “sandwich,” either PNP or NPN. As such, transistors register as two diodes connected back-to-back when tested with a multimeter's “resistance” or “diode check” function

## Slide 7
Electrical Switching on P-N Junction
Applying External Voltage…
…of Forward Biasing polarity facilitates motion of free electrons
…of Reverse Biasing polarity impedes motion of free electrons
Reverse Biasing
Forward Biasing
Circuit is “Off”
Current not Flowing
Circuit is “On”
Current is Flowing

## Slide 8: BJT introduction
BJT = Bipolar Junction Transistor
A BJT consists of two back-to-back p-n junctions.
The three regions are the emitter(E),base(B),and collector(C).
The middle region, the base is very thin. Since the base is thin, most carriers from emitter injected into base diffuse into collector.

## Slide 9
NPN
PNP
  NPN:
    BE forward biased
    BC reverse biased
  PNP:
    BE reverse biased
    BC forward biased
BJT schematic

## Slide 10: BJT formulae
NPN
Current control
β is the amplification factor and ranges from 20 to 200
It is dependent on temperature and voltage
Notes: Suggestion: state the qualitative definition behind these equations: when ib =0, when ib !=0, etc, what happens?

## Slide 11: BJT formulae
NPN
Emitter is more heavily doped than the collector.
Therefore,
VC > VB > VE
for NPN transistor
Notes: Why do more heavily doped (less electrons, more electrons) are of less/more voltage? Write it on the slide. Change the font. Change the background. b/c e is heavily doped…lower potential

## Slide 12: BJT formulae
NPN
α is the fraction of electrons that diffuse across the narrow base region
1 – α is the fraction of electrons that recombine with holes in the base region to create base current

## Slide 13: BJT Characteristic Curves
Transfer Characteristic
The graph of ICE / IBE shown (right) is called the Transfer Characteristic
The slope of the graph shows the β
Characteristic curves (graphs) can be drawn to show other parameters of a transistor, and are used both to detail the performance of a particular device and as an aid to the design of amplifiers.

## Slide 14: BJT Characteristic Curves
Input Characteristic
The Input Characteristic is the base emitter current IBE against base emitter voltage VBE(IBE/VBE) shows the input Conductance of the transistor.
The steepness of this particular curve when the VBE is above 1 volt shows that the input conductance is very high, and there is a large increase in current (in practice, usually enough to destroy the transistor!) for a very small increase in VBE.
Therefore the input RESISTANCE must be low.

## Slide 15: BJT Characteristic Curves
Output Characteristic
The slope gives the value of output conductance (and by implication output resistance).
The near horizontal parts of the graph lines show that a change in collector emitter voltage VCE has almost no effect on collector current in this region, just the effect to be expected if the transistor output had a large value resistor in series with it.
Therefore the graph shows that the output resistance of the transistor is high.

## Slide 16: BJT operating regions
Operating Region | Parameters | Mode
Cut Off | VBE < Vcut-in VCE > Vsupply IB = IC = 0 | Switch OFF
Linear | VBE = Vcut-in Vsat < VCE < Vsupply IC = β*IB | Amplification
Saturated | VBE = Vcut-in, VCE < Vsat IB > IC,max, IC,max > 0 | Switch ON

## Slide 17: The Transistor as A Switch
While there are limitations as to what we can switch on and off, transistor switches offer lower cost and substantial reliability over conventional mechanical relays.
The secret to making a transistor switch work properly is to get the transistor in a saturation state

## Slide 18: The Transistor as A Amplifier
Transistor Connections
Because an amplifier must have two input and two output terminals, a transistor used as an amplifier must have one of its three terminals common to both input and output as shown on the right. The choice of which terminal is used as the common connection has a marked effect on the performance of the amplifier.
There are three connection modes:
Comm0n Emitter Mode
Common Collector Mode
Common Base Mode

## Slide 19: The Transistor as A Amplifier
Parameter | Common Emitter | Common Collector | Common Base
Voltage gain Av | High (about 100) | Unity (1) | Medium (10-50)
Current Gain | High (50 - 800) | High (50 -800) | Less than unity (<1)
Input Impedance | Medium (about 3 to 5k) | High (several k) | Low (about 50R)
Output Impedance | Medium, Approx = Load resistor value | Low (a few ohms) | High (about 1M)
Summary of the three types transistor connection

## Slide 20: Several Comments about Transistor
Bipolar transistor consists of two PN junctions, with two types: NPN and PNP
BJT is a current control device.
The ratio of currents leads to one of the most important parameters of a transistor, which is its “current gain”, often referred to as its “Beta”.
BJT itself does not generate extra energy for amplifying, it just uses small current change to control big current change, which comes from the power supply.

## Slide 21: The Common Emitter Amplifier
NPN Transistor
- Both the signal source and the load share the emitter lead as a common connection point
- The common emitter configuration lends itself to voltage amplification and is the most common configuration for transistor amplifiers.