## Slide 1: Week 4
Introduction to Electric Circuits

## Slide 2: Agenda
Node Analysis (Text 4.1 - 4.4)
  Node Analysis with voltage sources
  Node Analysis with current sources and voltage sources (independent and dependent sources)
Mesh Analysis
  Mesh Analysis with voltage sources
  Mesh Analysis with current sources and voltage sources (independent and dependent sources)
LTSpice verifications
(DESIGN PROBLEM CONCEPT TO RECALL: BOUNDARY CONDITIONS)
Reference: UW, UH

## Slide 3: Node Analysis Applications

## Slide 4: Ground work
Node: a place where two or more components meet
Essential Node: a place where three or more components meet
Reference Node: A special essential node that we choose as a reference point for voltages
Super node: A combination of two or more nodes

## Slide 5: Node Analysis: Basics
Main point to remember: A Node is where two or more components meet. No matter how many wires are connected.

## Slide 6: Node Analysis: Basics
Main point to remember: A Node is where two or more components meet. No matter how many wires are connected.
In the example circuit schematic given here, there are three nodes. These nodes are shown in dark blue here.
Some students count more than three nodes in a circuit like this. When they do, it is usually because they have considered two points connected by a wire to be two nodes.

## Slide 7: Node Analysis: Basics
Main point to remember: A Node is where two or more components meet. No matter how many wires are connected.
In the example circuit schematic given here, there are three nodes. These nodes are shown in dark blue here.
Some students count more than three nodes in a circuit like this. When they do, it is usually because they have considered two points connected by a wire to be two nodes.
So this would be wrong

## Slide 8: Node Analysis: Step 1
Pick one node as reference node
It’s voltage will be defined/assumed to be zero

## Slide 9: Node Analysis: Step 2
Label the other nodes (Place where two or more components meet)

## Slide 10: Node Analysis: Step 3
Label the current through each node and use Ohm’s law and KCL for current equations at the nodes

## Slide 11: Node Analysis: Step 4
No equation for i7 as it is same as i1, net source current and solve for Node voltages.

## Slide 12: Example: from text
Find Va and Vb
We will solve as in the book
Two nodes based analysis using a and b, then super node ab.

## Slide 13: Example: from text
Find Va and Vb
We will solve as in the book
Two nodes based analysis using a and b, then super node ab.
ib
ia
is

## Slide 14: Verifying Answer
LT spice circuit

## Slide 15: Self Reading
Node voltage analysis using dependent voltage sources.
We will discuss it in class on need basis (Section 4.4 from book)

## Slide 16: Mesh Current Analysis
Provide step-by-step instructions for mesh analysis, which is a method to calculate voltage drops and mesh currents that flow around loops in a circuit.
Text Chapter sections 4.4 to Chapter 4.7

## Slide 17: What is Mesh Analysis Methodology
Technique to find voltage drops around a loop using the currents that flow within the loop, Kirchoff’s Voltage Law, and Ohm’s Law
  First result is the calculation of the mesh currents
    Which can be used to calculate the current flowing through each component
  Second result is a calculation of the voltages across the components
    Which can be used to calculate the voltage at the nodes.

## Slide 18: What is a Mesh
Mesh – the smallest loop around a subset of components in a circuit
Multiple meshes are defined so that every component in the circuit belongs to one or more meshes

## Slide 19: Step 1: Identify All Meshes

## Slide 20: Step 2: Label all currents

## Slide 21: Step 3: Label all voltages

## Slide 22: Step 4: Start solving for currents

## Slide 23: Step 5: Solve for Mesh Currents
Write mesh currents as individual components currents
Once mesh currents are known we can find voltage across components.

## Slide 24: Example further

## Slide 25: From previous analysis

## Slide 26: Rearranging
Mesh Currents | (mA)
i1 | 740
i2 | 264

## Slide 27: Final Values
Voltage across resistors | (V)
VR1 = -i1R2 | -2.96
VR2 = i2 R2 | 5.92
VR3 =(i1 – i2) R3 | 2.39
VR4 = i2 R4 | 1.59
VR5 = (V4 – V5) | 0.804
VR6 = (V5 – 0V) | 0.740
Currents | (mA)
IR1 = i1 | 740
IR2 = i1 | 740
IR3 = i1- i2 | 476
IR4 = i2 | 264
IR5 = i2 | 264
IR6 = i1 | 740
I Vin = i1 | 740

## Slide 28: Verification