## Slide 1: Week 5
Introduction to Electrical Circuits

## Slide 2: Appendix - I
  Recommendation:
    Use nodal analysis for circuits with fewer nodes than meshes, and use mesh analysis for circuits with fewer meshes than nodes.
  How many nodes does this circuit have?
  How many meshes?
Should You Use Nodal Analysis or Mesh Analysis?

## Slide 3: Appendix - II
For advancement in circuit analysis use all skills you obtain.
Graph theory
  Take advantage of topology
Node-voltage approach
  Aim to find all tree voltages initially
Loop-current approach
  Aim to find all branch currents initially
Note: From Node and Mesh Analysis, the final homework assignment is posted on Canvas. Last problem requires you to use LTSpice to simulate the circuit and verify the results. Please submit your LTSpice Image file and the resulting values using DC .op analysis (same as I did in class demo)

## Slide 4: Agenda
Source Transformations
Thevenin’s Theorem
Norton’s Equivalent Circuit
Superposition
Maximum Power Transfer
LTSpice Simulation of Equivalent Circuits
(Ref: This section is directly based on material from chapter 5 of text, UW, and VirginiaTech EE department resources)

## Slide 5: Source Transformation
We primarily deal with two kind of sources :
  Voltage and Current Sources
For our analysis we have always thought of them to be ideal.
Voltage source was supposed to be with no internal resistance, so it
Supplied its rated voltage value over time.
Its voltage stayed same as the power supplied from this source increased.
Current source was supposed to exhibit no leakage
It supplied constant/same value of current always in our circuit
Its current stayed same as the power supplied from this source increased.

## Slide 6: Source Transformation
Realistic or practical voltage source has some inherent resistance.
Because it impedes the current and decreases the voltage drop across terminals it can be viewed as an ideal source with series resistance
Realistic or practical current source has current leakage.
Because it decreases current with increasing power, it can be viewed as an ideal source with parallel resistance.
The best part - these are interchangeable
(Hence “transformation”)

## Slide 7: Source Transformation: Step 1
Find out the series resistance of the non-ideal source.
This is typically done by calculating voltage at open circuit condition first.
Then moving on from open circuit to maximum current value where voltage across the terminals of the source becomes negligible.
The slope of the V-I curve gives us the resistance value.

## Slide 8: Source Transformation: Step 2
Compute the value of source current by dividing the labeled/open circuit voltage with this computed resistance.
This becomes the new source current.
Put the same resistance value in parallel with this source.

## Slide 9: Source Transformation: In Class Exercise
Take a Voltage source with 2k Ohm resistance connected to its terminals. We know it’s internal resistance is 6k Ohm
Convert it to a current source, and then compare Va and Vb

## Slide 10: Thévenin’s Theorem
A linear two-terminal circuit can be replaced with an equivalent circuit of an ideal voltage source, VTh, in series with a resistor, RTh.
  VTh is equal to the open-circuit voltage at the terminals.
  RTh is the equivalent or input resistance when the independent sources in the linear circuit are turned off.

## Slide 11: Circuit Schematic: Thévenin’s Theorem

## Slide 12: Definitions for Thévenin’s Theorem
Linear circuit is a circuit where the voltage is directly proportional to the current (i.e., Ohm’s Law is followed).
Two terminals are the 2 nodes/2 wires that can make a connection between the circuit to the load.

## Slide 13: Definitions for Thévenin’s Theorem
Open-circuit voltage Voc is the voltage, V, when the load is an open circuit (i.e., RL = ∞W).
+
Voc
_

## Slide 14: Definitions for Thévenin’s Theorem
Input resistance is the resistance seen by the load when VTh = 0V.
It is also the resistance of the linear circuit when the load is a short circuit (RL = 0W).

## Slide 15: Steps to Determine VTh and RTh
Identify the load, which may be a resistor or a part of the circuit.
Replace the load with an open circuit .
Calculate VOC. This is VTh.
Turn off all independent voltage and currents sources in the linear 2-terminal circuit.
Calculate the equivalent resistance of the circuit. This is RTh.
  The current through and voltage across the load in series with VTh and RTh is the load’s actual current and voltage in the original circuit.

## Slide 16: Norton’s Theorem
A linear two-terminal circuit can be replaced with an equivalent circuit of an ideal current source, IN, in parallel with a resistor, RN.
  IN is equal to the short-circuit current at the terminals.
  RN is the equivalent or input resistance when the independent sources in the linear circuit are turned off.

## Slide 17: Circuit Schematic: Norton’s Theorem
Short-circuit current Isc is the current, i, when the load is a short circuit (i.e., RL = 0W).

## Slide 18: Definitions for Norton’s Theorem
Input resistance is the resistance seen by the load when IN = 0A.
It is also the resistance of the linear circuit when the load is an open circuit (RL = ∞W).

## Slide 19: Steps to Determine IN and RN
Identify the load, which may be a resistor or a part of the circuit.
Replace the load with an open circuit .
Calculate ISC. This is IN.
Turn off all independent voltage and currents sources in the linear 2-terminal circuit.
Calculate the equivalent resistance of the circuit. This is RN.
  The current through and voltage across the load in parallel with IN and RN is the load’s actual current and voltage in the original circuit.

## Slide 20: Source Conversion
A Thévenin equivalent circuit can easily be transformed to a Norton equivalent circuit (or visa versa).
  If RTh = RN, then VTh = RNIN and IN = VTh/RTh

## Slide 21: Voltage Polarity and Current Flow

## Slide 22: Value of Theorems
Simplification of complex circuits.
  Used to predict the current through and voltage across any load attached to the two terminals.
  Provides information to users of the circuit.

## Slide 23: Example #1

## Slide 24: Example #1 (con’t)
Find IN and RN

## Slide 25: Example #1 (con’t)
Calculation for IN
Look at current divider equation:
If RTh = RN= 1kW, then IN = 6mA

## Slide 26: Why chose RTh = RN?
Suppose VTh = 0V and IN = 0mA
  Replace the voltage source with a short circuit.
  Replace the current source with an open circuit.
  Looking towards the source, both circuits have the identical resistance (1kW).

## Slide 28: Source Transformation
Equations for Thévenin/Norton Transformations
VTh = IN RTh
IN = VTh/RTh
RTh= RN

## Slide 29: Example #1: Norton’s Theorem
IN = VTh/RTh = 6mA
IN is the current that flows when a short circuit is used as the load with a voltage source

## Slide 30: Example #1: Norton’s Theorem
RN is the resistance of the linear circuit when the power sources in the original circuit are turned off (VTh is replaced with a short circuit).

## Slide 31: Example #1: Norton’s Theorem
The Norton equivalent circuit is:

## Slide 32: Check: Thévenin Theorem
VTh = IN RTh = 6V
VTh is the voltage across the load when an open short circuit is used as the load with a current source

## Slide 33: Check: Iload and Vload

## Slide 34: Example #2
Simplification through Transformation

## Slide 35: Example #2 (con’t)

## Slide 36: Example #2 (con’t)
Find Req to obtain a Norton equivalent circuit

## Slide 37: Example #2 (con’t)
RTh = 3W
VTh = 0.1A (3W) = 0.3V
Current Source to Voltage Source

## Slide 38: Example #2 (con’t)
0.3V

## Slide 39: Example #2 (con’t)
RTh = 2W
IN = 3V/2W = 1.5A
Voltage Source to Current Source

## Slide 40: Example #2 - Solution 1
0.3V
Simplify to Minimum Number of Current Sources

## Slide 41: Example #2 (con’t)
RTh = 6W
IN = 0.3V/6W = 50.0mA
0.3V
Voltage Source to Current Source

## Slide 42: Example #2 (con’t)

## Slide 43: Example #2 (con’t)
Current Sources in Parallel Add

## Slide 44: Example #2 (con’t)
Transform solution for Norton circuit to Thévenin circuit to obtain single voltage source/single equivalent resistor in series with load.

## Slide 45: LTSpice

## Slide 46: Summary
Thévenin and Norton transfomrations are performed to simplify a circuit for analysis and design.
  Two techniques were described.
    Examples using the source transformation technique were given.

## Slide 47: Superposition
The voltage across a component is the algebraic sum of the voltage across the component due to each independent source acting upon it.
The current flowing through a component is the algebraic sum of the current flowing through component due to each independent source acting upon it.

## Slide 48: Superposition - Application
Transistor/MicroElectronics circuit analysis
Separating the contributions of the DC and AC independent sources.
Example:
  To determine the performance of an amplifier, we calculate the DC voltages and currents to establish the bias point.
  The AC signal is usually what will be amplified.
  A generic amplifier has a constant DC operating point, but the AC signal’s amplitude and frequency will vary depending on the application.

## Slide 49: Steps
Turn off all independent sources except one.
Redraw circuit.
Solve for the voltages and currents in the new circuit.
Turn off the active independent source and turn on one of the other independent sources.
Repeat Steps 2 and 3.
Continue until you have turned on each of the independent sources in the original circuit.
To find the total voltage across each component and the total current flowing, add the contributions from each of the voltages and currents found in Step 3.

## Slide 50: Turning Off Sources
Voltage sources should be replaced with short circuits.
  A short circuit will allow current to flow across it, but the voltage across a short circuit is equal to 0V.
Current sources should be replaced with open circuits.
  An open circuit can have a non-zero voltage across it, but the current is equal to 0A.
Once you select a direction for current to flow through a component and the direction of the polarity (+ /_ signs) for the voltage across a component, you must use the same directions when calculating these values in all of the subsequent circuits.

## Slide 51: Example #1

## Slide 52: Example #1 (con’t)
Replace Is1 and Is2 with open circuits

## Slide 53: Example #1 (con’t)
Since R2 is not connected to the rest of the circuit on both ends of the resistor, it can be deleted from the new circuit.
Redraw circuit without R2 in it.

## Slide 54: Example #1 (con’t)
Vs

## Slide 55: Example #1 (con’t)
Replace VS with a Short Circuit and Is2 with an Open Circuit
IS1
Redraw circuit.

## Slide 56: Example #1 (con’t)
Note: The polarity of the voltage and the direction of the current through R1 has to follow what was used in the first solution.
IS1

## Slide 57: Example #1 (con’t)
IS1

## Slide 58: Example #1 (con’t)
IS1

## Slide 59: Example #1 (con’t)
Replace VS with a Short Circuit and Is1 with an Open Circuit
IS2

## Slide 60: Example #1 (con’t)
Since V1 = -V3, but I1 must equal I3, the only valid solution is when I1 = I3 = 0A.
R2 and I2 are not in parallel with R1 and R3.
IS2

## Slide 61: Example #1 (con’t)
IS2

## Slide 62: Example #1
 | Vs on | Is1 on | Is2 on | Total
I1 | +42.9mA | +0.286A | 0A | +0.329A
I2 | 0 | -1A | 2A | +1A
I3 | +42.9mA | -0.714A | 0A | -0.671A
V1 | +2.14V | +14.3V | 0V | 16.4V
V2 | 0V | -30V | + 60V | +30.0V
V3 | 0.857V | -14.3V | 0V | -13.4V
Currents and voltages in original circuit with all sources turned on.

## Slide 63: LTspice Simulation

## Slide 64: Summary
Superposition can be used to reduce the complexity of a circuit so that the voltages and currents in the circuit can be determined easily.
  To turn off a voltage source, replace it with a short circuit.
  To turn off a current source, replace it with an open circuit.
  Polarity of voltage across components and direction of currents through the components must be the same during each iteration through the circuit.
  The total of the currents and voltages from each iteration is the solution when all power sources are active in the circuit.

## Slide 65: Maximum Power Transfer
For any power source, the maximum power transferred from the power source to the load is when the resistance of the load RL is equal to the equivalent or input resistance of the power source (Rin = RTh or RN).
  The process used to make RL = Rin is called impedance matching.

## Slide 66: Power Transfer Calculation
RTh 50W
VTh
1V

## Slide 67: Application
When developing new circuits for a known application, optimize the power transfer by designing the circuit to have an input resistance close to the load resistance.
When selecting a source to power a circuit, one of the selection criteria is to match the input impedance to the load resistance.

## Slide 68: Other Examples
Selection of wire –
  Antenna wire is designed to match a 75 W load.
  Coaxial cable is designed to act like a 50 W load.
Most electronic and electrical equipment are designed to have an RTh of 50 W.
  The speakers used in some of the ECE labs are designed to act like an an 8 W load while microphones are designed to act like a 600 W load.
    It is important that the resistance of the wire that runs to the speaker is very low or the power will be dissipated in the wire rather than used to create sound.
    For best audio quality, the input impedance of the circuit connected to the speaker (or the microphone) should be equal to the resistance of the speaker (or the microphone).

## Slide 69: Summary
Maximum power transfer theorem is used frequently to insure that the greatest power can be transferred from a power source to a load.